## Slide 1: Satellite Derived Bathymetry - Irma impact and integration with acoustic surveys -
2017-12-01
Dr. Knut Hartmann
hartmann@eomap.de
EOMAP GmbH & Co.KG
Germany | Australia| USA
www.eomap.com

## Slide 2: Satellite derived information
Remote measure
Global coverage of imagery
Rapid access to data
Satellite measure all parameters from sun to surface to satellite sensor (atmosphere, surface properties, etc)

## Slide 3
Satellite Derived Bathymetry Mtwarba region, Tanzania
18m
35km
Satellite data = f(atm., adjacency, water surface, aborbers and backscatterers of the water column, seafloor, water depth, seastate, sun and sensor geometry, SNR ratio)

## Slide 4
Seafloor reflectance
drapped over Satellite Derived Bathymetry
18m
35km
Satellite data = f(atm., adjacency, water surface, aborbers and backscatterers of the water column, seafloor, water depth, seastate, sun and sensor geometry, SNR ratio)

## Slide 5
Seafloor habitat classification
drapped over Satellite Derived Bathymetry
seagrass
corals
sediment
macroalgal
Coral rubble
Object based classification considering texture, shape and spectra of seafloor reflectance in addition to seabed morphology.

## Slide 6: Impact assessment of “Irma” and satellite information as rapid response tool

## Slide 7: Irma, Sept 2017
Image courtesy: The Economist, 2017. Image modified

## Slide 8: Turks and Caicos, Big Sandy Cay
Before
After
After
Before
Changes in very shallow water bathymetry with sandy bottom
Changes in coastline
Island was split into 2 parts now
Coral structure and geomorphology not significantly impacted
Irma

## Slide 9: Turks and Caicos, Big Sandy Cay
Before Irma
After Irma
Decrease of seagrass cover

## Slide 10: Punta de Maisi, East Cuba
before
after
Decrease of seagrass cover forereef
Small changes in coral structure
Coral/hardbottom seafloor and bathymety areas were not impacted by Irma
Natural dynamic of seafloor dominates Irma impacts
Irma

## Slide 11: Varadero Peninsula, Cuba
Satellite Derived Bathymetry: Rapid provision of up-to date bathymetric data grids
We‘re
here

## Slide 12: Varadero Peninsula, Cuba
We‘re
here
Satellite Derived Bathymetry: Generation of shallow water bathymetry for Varadero region in <24 hours

## Slide 13: Key messages
Satellite Derived Bathymetry allows rapid assessment of changes in coastline, seafloor cover / benthic habitats and shallow water bathymetry.
Method can work remote as rapid assessment tool but can also be integrated in survey concepts with acoustic data -> next section

## Slide 14: Integration of Satellite Derived Bathymetry with acoustic survey data

## Slide 15: Integrated approach of using SDB and Single Beam
Single Beam transects (AUV)
Very high resolution satellite image

## Slide 16: Integrated approach of using SDB and Single Beam

## Slide 17: Integrated approach of using SDB and MBES
0m
20m
X m
Satellite Derived Bathymetry
MBES survey
Overlapping region
British Admiralty Chart BA 2066
Southern Antigua
Calibration & Validation area

## Slide 18: Key messages
Combining SDB and single beam transects allows to provide a validated bathymetric dataset with full seafloor coverage, including very shallow waters.  This combination allows to minimize survey work while improving spatial coverage. High potential for rapid response surveys.
Combining SDB and MBES surveys allows to calibrate and validate SDB in the overlapping regions and results in a validated bathymetric dataset from deep waters to shoreline
 This combination allows to minimize cost intensive very shallow water surveys, reduces HSE risks while generating seamless bathymetric datasets from deep waters to shoreline

## Slide 19
Muchas gracias!
Dr. Knut Hartmann
hartmann@eomap.de
www.eomap.com
Satellite data recorded Nov. 2017, Varadero area, Cuba